## Slide 1: Applicability of Abstraction and Control of Traffic Engineered Networks (ACTN) to Packet Optical Integration (POI) draft-ietf-teas-actn-poi-applicability-08
Authors
Fabio Peruzzini – fabio.peruzzini@telecomitalia.it
Jean-Francois Bouquier – jeff.bouquier@vodafone.com
Italo Busi – Italo.busi@huawei.com
Daniel King – daniel@olddog.co.uk
Daniele Ceccarelli – dceccare@cisco.com
Contributors
Sergio Belotti – sergio.belotti@nokia.com
Gabriele Galimberti – ggalimbe56@gmail.com
Zheng Yanlei – zhengyanlei@chinaunicom.cn
Anton Snitser – asnizar@cisco.com
Washington Costa Pereira Correia – wcorreia@timbrasil.com.br
Michael Scharf – michael.Scharf@hs-esslingen.de
Young Lee – younglee.tx@gmail.com
Paolo Volpato – paolo.volpato@huawei.com
Jeff Tantsura – jefftant.ietf@gmail.com
Brent Foster – brfoster@cisco.com
Oscar Gonzalez de Dios – oscar.gonzalezdedios@telefonica.com

## Slide 2: I-D Use Cases
  1. Inventory, Service and Topology Discovery
      Inter-domain link discovery
      Multi-layer IP Link discovery
      Inventory discovery
      TE paths discovery
  2. Establishment of L2VPN/L3VPN with TE requirements
      Optical Path Computation
      Multi-layer IP Link Setup and Update
      TE Path Setup and Update
Packet Domain 1
Packet-PNC 1
Optical-PNC 1
Optical-PNC 2
Packet-PNC 2
MDSC
Packet Domain 2
Optical Domain 1
Optical Domain 2
CE
CE
PE
BR
BR
PE
Figure 1 - Reference Scenario

## Slide 3: Status
Updates in version 08
  Generalized description of SR-TE path discovery, setup and update: applicable to any technology to which IETF TE Tunnel model can be used at the MPI
    MPLS-TE and SR-TE are just examples of technology-specific augmentations
    SR-TE covers both SR-MPLS and SRv6
    BGP-LU inter-domain option (RFC3107) outside the scope
  Editorial updates
Issue tracking and current version available on Git
  https://github.com/FabioPeruzzini/actn-poi/issues
  Most of them just requires writing text
  Few requires feedbacks from TEAS WG: see next slides

## Slide 4: Open Issue #45 – SRLGs
The SRLG value does not provide information about the type of risk (e.g., Conduit SRLG, Transponder SRLG, ROADM degree SRLG or ROADM node SRLG)
  Not an issue for the SRLG disjointness path computation
  But there are cases where the operator is willing to know the type of SRLG for other management purposes
The ietf-te YANG model defines named SRLGs
  Could this construct be used to address the issue?
  Not clear the definition of the cost associated with a named SRLG
Proposal: describe this as a gap to be addressed in another document

## Slide 5: Open Issue #36 – Optical Transparent Services
Current draft text assumes that the Optical Network provides Ethernet frame-based service
  In most of the existing deployments the Optical Network provides Transparent CBR services
Not sure the description can be generalized to cover both frame-based and transparent services (see next slide)
Proposal: try to generalize the description, if possible, otherwise describe the transparent services cases

## Slide 6
Optical Topology (O-PNC 1)
NE11
NE14
Ethernet Topology (P-PNC 1)
Supporting LTP
PE13
BR11
Transparent Client Signal
Optical Tunnel
Undelay tunnel
IP Topology (P-PNC 1)
Supporting LTP
PE13
BR11
Supporting LTP
Supporting LTP
Multi-layer Intra-domain IP Link setup
3) The multi-layer ETH link is either discovered by P-PNC1 or configured by the MDSC
4) The IP link is created by the MDSC but fully configured by P-PNC1
1) The Optical Tunnel is configured by the MDSC and setup by O-PNC1
2) The Transparent Client Signal is configured by the MDSC and NEs are properly configured by O-PNC1
No Ethernet Topology exposed by O-PNC

## Slide 7: ACTN POI Next Steps - Overview
ACTN POI (step 1)
Inventory, Service and Topology Discovery
Establishment of L2VPN/L3VPN with TE requirements
ACTN POI (step 2a) – service assurance
Optical Network failures and degradation
IP/Optical Edge failures
ACTN POI (step 2b) – pluggable
Pluggable WDM interfaces on routers
Same scenarios as in step 1
TEAS WG
CCAMP WG

## Slide 8: Next Steps for this draft
Planned updates to the document
  Update the text to address all the open issues
  Editorial and terminology clean-up
  Improve Security section
Resuming weekly ACTN POI calls after IETF 116
  Starting from April 4 (slot 2)
  Working also in parallel on steps 2a and 2b
Be ready for WG Last Call before IETF 117